| Date inspected: By: | Treatment ID/Name: With: |
| --- | --- |
| How many cylinders are on site? full partial empty Gas chlorine feed rate: lbs/day Water flow rate: gpm Calculated chlorine feed rate: mg/l Measured chlorine residual at EP: mg/l free mg/l total | Photos |
| *Is chlorine residual within range: 0.2 mg/l < X < 4.0 mg/l *Is chlorine residual checked daily and recorded? Is a manifold provided to allow feeding gas from more than one cylinder? Is there automatic switchover from cylinder to cylinder? Are scales provided for weighing of cylinders? Are all gas cylinders restrained near the top and about half way down by chaining to a wall or by other means? FOR GAS CHLORINATION STATION INSIDE A BLDG Are chlorine storage and use areas isolated from other work areas? Are stored cylinders capped and labeled? Is room ventilated to the outdoors with suction located no more than 6 inches above the floor? Is vent inlet near the ceiling? Is room containing chlorination equipment labeled sufficiently (DANGER signs, etc.)? Is a view port provided into the room storing chlorine? Is a means of leak detection provided? Type? Is a self-contained breathing apparatus available for use during repair of leaks? Where? Are personnel trained to use the apparatus? Are all doors hinged outward and equipped with panic bars? | Y N Unk N/A □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ |  |
| Notes: |  |