| Date inspected: By: | Location: With: |
| --- | --- |
| Entry point name: Average production: gpm | Photos |
| GWUDISW determination made? Is recharge area protected? If yes, how? Ownership Fencing Ordincaces Other: What is the nature of the recharge zones? Agricultural Industrial Forest Residential Other: Is the site protected from flooding? Is there diversion of surface drainage from site? Is collection chamber properly constructed? Does hatch cover overlap? Is the overflow outlet screened? Is supply intake adequate? Is site properly protected (from livestock, vandalism, tampering, etc.)? What conditions cause changes to quality of the water? | Y N Unk N/A □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ |  |
| Notes: |  |