| Date inspected: By: | Well ID: With: |
| --- | --- |
| The numbers in parenthesis like (§7.4) refer to CNMI Well Drilling and Well Operation Regulations paragraph numbers. If there is no paragraph cited, then the question/concern is from standard sanitary survey guidance from EPA. | Photos |
| Is the site protected against trespass/vandalism (fenced)? Does surface runoff and underground drainage drain away (is the well site protected from flooding)? Is the well site protected from potential sources of contamination (includes: known chemical spills, agricultural uses, septic systems, etc.), and meet set back distances §6.1? Is there a concrete pad at least 3’ x 3’ x 6” (§7.3)? Does the casing extend 12” above concrete pad (§6.10)? Is the top of the well casing properly sealed (sanitary seal) §7.2b.)? Is there a 1” PVC sounding tube that is 6” higher than the well casing, and capped to prevent contaminants from entering well (7.2a)? Is there a vent equipped with a stainless steel insect screen with a downward “U” bend (§7.2)? Is there a working: Pressure gauge (§7.4)? psi Check valve (§7.4)? Gate valve (§7.4)? Sample tap (§7.4)? Flow meter (§7.4)? gpm Is the pressure gauge and flow meter read and recorded daily? Is the electric wiring from the control panel to the well head in conduit (does it meet electric code requirements)? | Y N Unk N/A □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ □ |  |
| Notes: |  |